## Slide 1
Video Imaging
Dr. Nelson Díaz
Departamento de Ingeniería Informática
Universidad Técnica Federico Santa María, campus Valparaíso, Chile
nelson.diazd@usm.cl
Academic website https://nelson-diaz.com/

## Slide 2
2
Computational Photography
Areas:
Computer Science
Electrical Engineering and Electronics
Maths
Physics (optics)

## Slide 3
3
Computational Photography
Goal:
To capture and recover singal in many dimensions
To design
Hardward
Software--algorithm to solve the inverse problem--

## Slide 4
4
Computational Photography: Applications
Multispectral
Video
It can be applied to different signals
It use compressive measurements
To solve an inverse problem
1995
Cubic Phase
Depth
A woman
GT phase
Recovered phase
Recovered Amplitude

## Slide 5
Single-mask sphere-packing with implicit neural representation for ultrahigh-speed imaging
Nelson Diaz1, Madhu Beniwal2, Miguel Marquez2, Felipe Guzman1, Cheng Jiang2, Esteban Vera1, Jinyang Liang2
1 School of Electrical Engineering, Pontificia Universidad Católica de Valparaíso, Valparaíso, Chile
2 Laboratory of Applied Computational Imaging, Centre Énergie Matériaux Télécommunications, Institut National de la Research Scientifique, Montreal, Canada

## Slide 6
Sensing Transient Events
Neuroscience for monitoring neural activity
Nuclear fusion: Fast-heating plasma
R. Kodama, P. Norreys, K. Mima, A. Dangor, R. Evans, H. Fujita, Y. Kitagawa, K. Krushelnick, T. Miyakoshi, N. Miyanaga et al., “Fast heating of ultrahigh-density plasma as a step towards laser fusion ignition,” Nature 412, 798–802 (2001)
X. Zhu, Q. Huang, A. DiSpirito, T. Vu, Q. Rong, X. Peng, H. Sheng, X. Shen, Q. Zhou, L. Jiang et al., “Real-time whole-brain imaging of hemodynamics and oxygenation at micro-vessel resolution with ultrafast wide-field photoacoustic microscopy,” Light. Sci. & Appl. 11, 138 (2022).
Conventional cameras capture up to 107

## Slide 7
Active and Passive illumination
Jinyang Liang and Lihong V. Wang, "Single-shot ultrafast optical imaging," Optica 5, 1113-1127 (2018)
Active-detection
Passive-detection
A pulse probe for a transient event.
An optical marker e.g. spatial division, or angle division divide the transmitted probe pulses
After the transient scene in the spatial frequency domain to recover the 3D spatio-temporal datacube.
Passive detection can overcome active illumination.
The detector only receive and record the emitted and/or scattered photons from the scene.

## Slide 8
Single snapshot compressive spectral imaging
Ashwin Wagadarikar, Renu John, Rebecca Willett, and David Brady, "Single disperser design for coded aperture snapshot spectral imaging," Appl. Opt. 47, B44-B51 (2008)
The scene is encoded using a binary coded aperture. Then, the encoded scene is sheared by the temporal shearing operator. The encoded and sheared scene is captured in the detector.

## Slide 9
Compressive Ultrafast Photography (CUP)
L. Gao, J. Liang, C. Li, and L. V. Wang, “Single-shot compressed ultrafast photography at one hundred billion frames per second,” Nature 516, 74–77 (2014).
The scene is encoded using a binary coded aperture. Then, the encoded scene is sheared by the temporal shearing operator. The encoded and sheared scene is captured in the detector.
It is a passive-detector approach

## Slide 10
Compressive Ultrafast Photography (CUP) Applications
Single-shot CUP pulse refraction
Optical Mach cone using CUP
L. Gao, J. Liang, C. Li, and L. V. Wang, “Single-shot compressed ultrafast photography at one hundred billion frames per second,” Nature 516, 74–77 (2014).
Real-time applications is limited by reconstruction

## Slide 11
Representación neuronal implicita para video ultrarápido
N. Diaz, M. Beniwal, M. Marquez, F. Guzmán, C. Jiang, J. Liang, and E. Vera, “Single-mask sphere-packing with implicit neural representation reconstruction for ultrahigh-speed imaging,” Optics Express 33, pp. 24027–24038, 2025.

## Slide 12
COSUP Discrete Model
traditional coded aperture
measurement
video
designing the encoding is critical for real-time applications

## Slide 13
Discrete model
coded aperture
measurements
video
novel aperture design

## Slide 14
What is Sphere Packing?
Ask for the densest packing of
Faced-center cubic lattice is optimal in 3D
stacking cannonballs
Tiling the space by replicating the unit cell
J. Kepler, The six-cornered snowflake (Paul Dry Books, 2010).
T. Hales, M. Adams, G. Bauer, T. D. Dang, J. Harrison, H. Le Truong, C. Kaliszyk, V. Magron, S. McLaughlin, T. T. Nguyen, and et al., “A formal proof of the kepler conjecture,” Forum Math. Pi 5, e2 (2017).

## Slide 15
Coded Aperture Design
uniform sensing
uniform coded aperture
The coded aperture exploits the shifting induced by the galvanometer scanner.
Our design guarantees uniform sampling.

## Slide 16
Traditional Coded Aperture Design
Non-uniform sensing
Random coded aperture

## Slide 17
Sphere Packing Comparison Between DMDs
orthogonal DMD
diamond DMD
Texas instruments
orthogonal: DLP3010LC
diamond: DLP® 0.45 WXGA DMD

## Slide 18
Simulation Results

## Slide 19
Simulation Results

## Slide 20
Simulation Results

## Slide 21
Simulation Results
measurements
reconstruction
measurements
reconstruction
I. Amidror, “Scattered data interpolation methods for electronic imaging systems: a survey,” J. Electron. Imaging 11,157–176 (2002).

## Slide 22
Experimental implementation
Architecture: compressed optical-streaking ultra-high-speed photography
Encoding: single binary mask
Shearing operator: Galvanometer
(b)

## Slide 23
Real-data: Interpolation
31 frames
measurement
measurement
reconstruction
reconstruction
I. Amidror, “Scattered data interpolation methods for electronic imaging systems: a survey,” J. Electron. Imaging 11,157–176 (2002).

## Slide 24
Real-data with Implicit Neural Representation
reconstruction
reconstruction
reconstruction
V. Sitzmann, J. Martel, A. Bergman, D. Lindell, and G. Wetzstein, “Implicit neural representations with periodic activation functions,” in Advances in Neural Information Processing Systems, vol. 33 H. Larochelle, M. Ranzato, R. Hadsell, M. Balcan, and H. Lin, eds. (Curran Associates, Inc., 2020), pp. 7462–7473
Parameters
Initial learning rate: 0.0005
Iteration: 1500
Resolution: 714 x 574 x 31
Training: a single measurement
Training time: 1.7 s
Testing time: 2.5 ms
Layers: Two hidden layers

## Slide 25
Conclusions
We introduced a novel binary coded aperture for compressed optical-streaking ultra-high-speed photography
Our designed coded aperture samples uniformly the video
We recover the underlying video using interpolation and implicit neural representation
uniform sensing
uniform coded aperture